## Slide 1: Design & CAD Best Practices
李岱峰
2020.07.22

## Slide 2: Design
Requirements:
  Know Requirements (then prioritize requirements)
  Background Research (If exists, don’t redesign it)
  System calculation
  Component level research
  Constantly check system mass and space envelope
  Design reviews
ask for help if needed
Notes: link to good presentation as example for “design requirement”

## Slide 3: Collaborating Etiquette
Fully define the position of each part in assembly, unless visualization of motion needed for certain parts
Don’t push parts/assemblies when they are broken, fix what you break before you push
Use part library if available
Don’t release linked parts
Use “Weldment” feature for tube, 80/20, angle, and other structures made from “beam” elements.

## Slide 4: CAD Workflow
Example: SolidWorks PDM
Notes: Review on drawings before release

## Slide 5: Sketches (some are SW specific)
Fully define sketches. All BLACK, no BLUE.
  DO NOT use “Fully Define Sketch” button
Use equations, relations, and general variables
  Use relation definitions (for example, “=”), or define variables
Dimension rectangles from the edges, not the corner
Make separate features in separate sketch unless it’s master sketch from top-down
Use symmetrical relations
Put origin at a mounting location (or center point)
Use construction lines to help define sketch
3D Sketch - 2D first then having 3D sketch come off of that
Notes: Baseline dimensioning

## Slide 6: Sketch - Fully Define Sketches

## Slide 7: Sketch - Combine Common Dimensions

## Slide 8: Sketch - Dimensioning Rectangles
Notes: Example of why, what’s gonna happen if not

## Slide 9: Use Construction Lines
Also:
-Symmetrical Relation
-Origin

## Slide 10: 3D Sketch
SubT Frame Example
Initial 2D controlling sketch.
Detailed 3D Sketch based off of 2D Sketch
Weldment Feature Created from Both Feature

## Slide 11: Parts
Use symmetry whenever possible
Use configuration when possible (NOT PROGRESS RELATED)
Make features like when it’s being machined (block/cut)
Use design table
Name useful dimensions and features
  Especially when those dimensions are referenced
Make several simple features instead of one complicated feature. (More robust and easy to edit)
Use fillet features instead of sketch fillets
Apply cosmetic fillet and chamfer last
Notes: If slightly different, make it different for assembly as well (use the esymmetrical)
Configuration: for example - waterjet, undersize holes “waterjet config”

## Slide 12: Use Symmetrical Relations

## Slide 13: Use Configuration

## Slide 14: Make features Like Being Machined
Even better, if you dimension it as being machined

## Slide 15: Use Design Table
Notes: link to where to get the tutorial

## Slide 16: Label Important Dimensions

## Slide 17: Make Separate Features for Sketches
Notes: Hole wizard on the corner
Use folder structure

## Slide 18: Fillet in Feature Not Sketch if Possible

## Slide 19: Imported Components
Suppress threads
When downloading parts, choose the best type available
  In order: .sldprt, .sldasm, .igs, .step/stp (AP214), .step (AP203), .stl
Complete feature recognition the first time and save
  For modified purchased parts, put all original features in a feature folder to make clear what your changes are
For assembly, save as part if you can
  If you have to have an imported assembly, put it in a subfolder
Try to avoid surface models when possible
  Clean up surfaces with the “Delete and Patch” tool
Override mass property with catalog listed mass
Notes: explain why for the order the download type
“dissolve part” - Ralph solidwork 2018 for igs

## Slide 20: Assembly
Origin plane mates (especially first part)
If possible, mate all components to one or two fixed references
  Long chains of components take longer to solve and more likely to get errors.
  Do not create loops for mates
Fully define the position of each part in assembly, unless visualization of motion needed for certain parts
  Option: use mechanical mates
Patterns, not multiple same parts if possible (greatly reduce computing power needed)
Lock rotation on cylindrical mate

## Slide 21: Put Origin as Mount Location
Notes: Float first, and re-mate it

## Slide 22: Use Component Patterns
In addition, use the magic combo:
hole wizard
+
Pattern driven component pattern

## Slide 23: Pattern Driven Component Pattern

## Slide 24
https://www.solidsolutions.co.uk/solidworks/tutorial-videos/top-down-modelling-best-practice.aspx

## Slide 25: Bottom Up
Model parts about the origin
Mate with planes/references instead of features
Don’t link parts

## Slide 26: Top Down
Name key dimensions on master model
Create moveable blocks

## Slide 27: Reference Links
● http://help.solidworks.com/2018/English/SolidWorks/sldworks/c_Best_Practices_for_Mates_SWassy.htm?verRedirect=1
● https://blog.alignex.com/10-large-assembly-best-practices-in-solidworks
● https://forum.solidworks.com/thread/183132
● https://petercad.com/category/solidworks-best-practices/
● https://www.solidsolutions.co.uk/solidworks/tutorial-videos/top-down-modelling-best-practice.aspx